## Slide 1: Background - The VAMPIRES Instrument
Polarimetric aperture masking and imaging in the visible
  Aperture masking - Diffraction limited imaging through the atmosphere… …resolution of 10s mas
  Differential polarimetry - imaging scattered starlight
    Precision differential calibration beats the contrast problem (triple-differential)
    Measurement of dust grain type, size
‘Hitch-hiker instrument’ - operates on visible channel of SCExAO on Subaru telescope, simultaneous with IR observations (e.g. CHARIS)

## Slide 2: SCIENCE CASE: Imaging the inner region of proto-planetary disks at solar-system scales
Inner region (10’s of AU) critical for understanding planet formation and disk structure
Precise measurement of transition disk gaps and inner disk
Density perturbations from massive bodies within disk (e.g. warps, spirals)
Gravitationally bound clumping dust immediately surrounding forming planets
Dust grain species and size determination
Complementary to coronagraphy
Resolution ~10 mas; 0.5λ/D
  ~1 AU at 100 pc
NRM F.O.V. ~500 mas, PDI ~3 arcsec
Scattered starlight, not thermal
MWC758 - Base image: Grady et al., ApJ, 2013
Hydrodynamical modelling of gravitational collapse of protoplanetary disk, with resulting fragmentation causing gravitationally bound clumps Mayer L., et al., 2007, ApJ 661 77
Notes: Basically any dusty circumstellar environment. Obvious ones are protoplanetary disks and mass-loss shells, but could be other uses (eg AGN)

## Slide 3: SCIENCE CASE: Imaging the inner mass-loss region of evolved stars
Mass-loss process poorly understood
Ejected material comprises next generation of stars & planets
What drives this wind?
Directly image inner dust condensation region, explore grain size and composition (polarimetry)
Origin of asymmetries
Asymmetries observed at wide scales - where do they originate?
At star (effect of stellar atmosphere) or interstellar medium?
Extension of red giant atmospheres
Does radiative pressure on dust in atmosphere contribute to extension?
Peter Woitke: http://www.strw.leidenuniv.nl/~woitke/AGB_popular.html
W Hya light curve (AAVSO)

## Slide 4: Nuts and bolts: VAMPIRES within SCExAO
Subaru IR Nasmyth platform
AO188
SCExAO
HICIAO

## Slide 6
  New mode - Differential spectral line imaging - Hɑ, SII Operates double-differential to calibrate NCP

## Slide 7: Diffraction limited imaging through atmosphere: One method: Non-Redundant Masking
State of the art 10m telescope: - Diffraction limit ~ 10 mas - Seeing limited ~ 1000 mas
The goal: mitigate the effect of the turbulent atmosphere to allow diffraction limited, high contrast imaging.
Aperture masking interferometry present state of art
—> Each and every hole-pair is baseline of interferometer
—> Recover diffraction limited performance
y - Measured baseline phase
f - Actual baseline phase
e - error from atmosphere
y12 = f12 + e2
y23 = f23 + e3 - e2
y31 = f31 - e3
C.P. = y12 + y23 + y31 = f12 + f23 + f31
1
2
3
Visibilities - a power spectrum, independent of phase
Closure phase independent of phase

## Slide 8: Power spectrum example: annulus
Discrete sampling of Annulus PS Excellent Fourier coverage, arbitrarily short baselines.
Vega, 4s integration

## Slide 9: Differential calibration - in an ideal world…
H polarisation image ⭑ Error (seeing, systematics)
H polarisation visibilities x Error visibilities
FT
V polarisation image ⭑ Error (seeing, systematics)
V polarisation visibilities x Error visibilities
FT
÷
=
V/H polarisation visibilities
(CLEAN OBSERVABLE)

## Slide 10: Differential calibration - triple layer switching!
Address non-common-path & non-simultaneous errors

## Slide 11: Differential calibration - triple layer switching!
Address non-common-path & non-simultaneous errors
Polarising beamsplitter!
Half-wave Plate!
Liquid crystal variable retarder
1 2 quarter wave plates

## Slide 12: Differential calibration - triple layer switching!
Address non-common-path & non-simultaneous errors

## Slide 13: Differential calibration - triple layer switching!
Address non-common-path & non-simultaneous errors

## Slide 14: Necessary Technical note…
Effective way of plotting calibrated VAMPIRES data is with a polarised visibility ratio plot:
Synthetic example data
Y Axis:
Ratio of horizontally-polarised to vertically-polarised interferometric visibilities (Fourier power)
X Axis:
Azimuthal angle (on-sky) of the baseline (spatial frequency coordinate)
Color scale:
Baseline length (on-sky) (abs value value of spatial frequency coordinate)
2 plots: Correspond to Stokes Q and U coordinates
Should = 1 for all unpolarised targets…
Demonstrates calibration precision
Notes: Need to briefly explain this to understand next slide

## Slide 15: NRM mode CALIBRATION PERFORMANCE
Demonstrated polarised-differential NRM visibility calibration to 1 part in 10^3 per baseline.
  Roughly speaking, achievable contrast at 0.5𝜆/D (10 mas) goes as √nBaselines - DOF
Conventional 2-beam polarimetry
Triple-differential calibration

## Slide 16: NRM-MODE example Science-RESULT
Investigation of supergiant mass-loss via direct imaging of Circumstellar dust around Red Supergiant μ Cephei
Observed with annulus mask at 775 nm
Raw differential polarized visibilities show distinctive sinusoidal signature of circumstellar dust shell, with clear asymmetry (right)
Dust scattering model fitted via synthetic differential visibilities (below)

## Slide 17: NRM-MODE example Science-RESULT
Model-fitting reveals extended, asymmetric dust shell, originating within the outer stellar atmosphere, without a visible cavity. Such low-altitude dust (likely Al2O3) important for unexplained extension of RSG atmospheres.
Left: model image, shown in polarized intensity. Middle: model image show in four polarisations. Right: Model image (intensity), shown with wide field MIR image (from de Wit et al. 2008 – green box shows relative scales. Axis of extension in MIR image aligns with the close-in VAMPIRES image.
Inner radius: 9.3 ± 0.2 mas (which is roughly Rstar)
Scattered-light fraction: 0.081 ± 0.002
PA of major axis: 28 ± 3.7 ° • Aspect ratio: 1.24 ± 0.03

## Slide 18: Imaging/PDI mode
High-speed acquisition and polarisation switching rate (up to 500 Hz) - allows offline tip/tilt correction and ‘lucky imaging’ approach, unlike CCD-shuffle based systems
  Example: 750 nm PSF, 100 frames/sec, discard 80% lowest-Strehl frames, align and sum (~30 secs of data)

## Slide 19: Imaging/PDI mode
SCExAO yields excellent correction at visible wavelengths
  Example: basic alignment and top 20% of frames, acquired at 100 fps, played back at 25 fps

## Slide 20: IMAGING-MODE example Science-RESULT
Direct imaging of omi Cet - clear asymmetry seen.
  Speckle imaging - diffraction-limited
6 mas / px
FWHM = ~18 mas
𝛌 / D = 19.3 mas
omi Cet
Observed 12/09/2017
PSF ref (63 Cet)
100 mas
100 mas

## Slide 21: IMAGING-MODE example Science-RESULT
Observation of omi Cet - dust shells and disk around omi Cet b observed
  Very preliminary reduction
Stokes Q
Stokes U
omi Cet b disk
omi Cet b disk
Inner shell ~ 2R★
Gap & 2nd shell
Inner shell ~ 2R★
Gap & 2nd shell
Dust transfer?
Observed 12/09/2017

## Slide 22: IMAGING-MODE example Science-RESULT
Effect of single vs triple polarisation calibration
Stokes Q
3-layer PDI

## Slide 23: IMAGING-MODE example Science-RESULT
fractional P
Stokes Q
Stokes U
Disk around AB Aur
100 mas

## Slide 24: IMAGING-MODE example Science-RESULT
Stokes Q
Stokes U
Disk around AB Aur
100 mas

## Slide 25: IMAGING-MODE example Science-RESULT
fractional P
Disk around AB Aur - poorer seeing

## Slide 26: IMAGING-MODE example Science-RESULT
Observation of AB Aur - new inner-regions of disk identified
  Preliminary reduction, optimal pipeline in development
Radial gap - real?